## Installation Guide for Radio Module RMS using Jooby Mobile App
To install Radio module with sensor for gas meter (here and after - Radio module) in this case please follow next steps:
1. Shut off the resource supply through the meter (gas).
2. Go to the app. On the Installation list screen, click Add (+) in the bottom right corner of the screen.
3. In the app scanning window, scan the QR code or enter the serial number of the radio module (S/N row of the radio module marking data) manually.
4. On the New installation screen, please fill the information about your installation:
  1. Take a photo of the meter without mounted radio module. Important! The photo should clearly read the meter readings. ou may take a photo of the meter without the mounted radio module after step 1 is done and download it from the Gallery.
  2. Resource type (gas)
  3. Manufacturer and model of the meter
  4. Serial number of the meter
  5. Meter readings at the moment of installation starting.
5. Mount the Radio module on the meter body as indicated on Pic.1a, 1b. Be sure that the radio module LED-status indicator flashes once shortly immediately after mounting and then it flashes shortly several times more in ~20 sec. Herewith activation of the radio module is done automatically.
6. Come back to the app on New installation and specify:
  1. Take a photo of the meter with the mounted radio module. mportant! The photo should clearly read the meter readings as well as the marking data of the radio module.
  2. Comments (optional).
7. Click Done on the screen of the mobile app.
  1. If the installation was successful, you can see a corresponding message. Click Finish job. The installation is finished.
If the radio module has not been activated, you can see Error message. Then the installation was not completed successfully. To retry the installation, repeat step 9 and click Try again.